Generic Packet Format

Each packet is formed by a Start-of-Transmission (SOT), the data, a Check-sum, and an End-of-Transmission (EOT). Following is the format for a data packet:

SOT1	SOT2	DATA	CHKSUM1	CHKSUM2	EOT1	EOT2
0xA5	0x5A				0xCC	0x33

The Check-sum evaluated as the last 2 bytes in the sum of all the bytes in the data portion of the packet.

An example of an engine RPM command follows:

SOT		DATA			CHKSUM		EOT
0xA5	0x5A	0x54	0x45	0x32	0x00	0xC6	0xCC	0x33

When the helicopter is responding to an order from the base station, the packet format is as follows:

SOT1	SOT2	ACK	DATA	CHKSUM1	CHKSUM2	EOT1	EOT2
0xA5	0x5A	0x06				0xCC	0x33

The ACK is not included in the check sum. This way, the base station can verify that everything transmitted was received correctly.

ACK's are only sent from the helicopter in response to commands from the base station that do not request information. For these commands, the telemetry sent will serve as the ACK.

Communications Hand-Shake

The handshake is transmitted periodically and is intended solely to prove good communications between the helicopter and the base station. The handshake is initiated by the base station, acknowledge by the helicopter and then terminated by the base station.

The data portions of the handshaking packets are shown below.

Initiate (by base station, sent until ACK received)
0x43	Command type “Communications”
0x48	Command “Handshake”

Acknowledge (by helicopter, sent until “Terminate” received)
0x43	Command type “Communications”
0x06	ACK

Terminate (by base station)
0x43	Command type “Communications”
0x54	Command “Terminate Handshake”

Testing/Tuning Commands

Engine RPM:
0x54	Command type “Testing/Tuning”
0x45:	Command “Engine RPM adjust”
0xVV:	Hex value from 0x00 to 0x64 representing the desired percentage of engine speed.

Pitch Cyclic – Cyc(P)
0x54	Command type “Testing/Tuning”
0x50:	Command “Pitch Servo adjust”
0xVV:	Hex value from 0x00 to 0x64 representing the desired Duty Cycle (DC) of the PWM controlling the Cyc(P) servo.

Roll Cyclic – Cyc(R)
0x54	Command type “Testing/Tuning”
0x52:	Command “Roll Servo adjust”
0xVV:	Hex value from 0x00 to 0x64 representing the desired Duty Cycle (DC) of the PWM controlling the Cyc(R) servo.

Collective
0x54	Command type “Testing/Tuning”
0x43	Command “Collective Servo adjust”
0xVV:	Hex value from 0x00 to 0x64 representing the desired Duty Cycle (DC) of the PWM controlling the Collective servo.

Anti-Torque
0x54	Command type “Testing/Tuning”
0x51	Command “Anti-torque Servo adjust”
0xVV:	Hex value from 0x00 to 0x64 representing the desired Duty Cycle (DC) of the PWM controlling the Anti-Torque servo.

Set Tune points
0x54	Command type “Testing/Tuning”
0xSS	Tuning set: 0x5A = Zero Points, 0x46 = 50% points, 0x4D = Max points
0xVV	Hex Value for Engine RPM percent
0xVV	Hex Value for Pitch Servo DC
0xVV	Hex Value for Roll Servo DC
0xVV	Hex Value for Collective Servo DC
0xVV	Hex Value for Anti-Torque Servo DC

Flight Operations Commands (commands sent to helicopter)

Engage Engine
0x46	Command type “Flight Ops”
0x45	Command “Engage Engine”

Hover
0x46	Command type “Flight Ops”
0x48	Command “Hover”
0xPP	Parameter set:
0x50 = Use preset altitude
0x43 = hover at current altitude
0x4D = use following altitude
0xAAAA	2-byte value representing desired hover height (used only when parameter set 0x4D is also used)

Go To
0x46	Command type “Flight Ops”
0x47	Command “Go To”

0xDD	Degrees (0-180) Latitude
0xMM	Minutes (0-59) Latitude
0xSSSS	Seconds(0-59) Latitude. Use upper six bits for integer portion of seconds, use remaining 10 bits for decimal portion of seconds. There are approximately 31 meters in one second of latitude (and slightly less in 1 minute of longitude at our distance from the equator). 31m / 2^10 = 3 cm accuracy, which is way more accuracy than the GPS will determine.
0xNS	0x4E = North
0x53 = South

0xDD	Degrees (0-180) Longitude
0xMM	Minutes (0-59) Longitude
0xSSSS	Seconds(0-59) Longitude. See above for more details.
0xEW	0x45 = East
0x57 = West

con't next page
0xAA	Action on Arrival:
0x48 0xAAAA	Hover at given altitude
0x53 0xNN	Conduct Search Pattern #NN

Return to Base (RTB)
0x46	Command type “Flight Ops”
0x52	Command “Return to Base”

Request Pre-flight Packet (PFP)
0x46	Command type “Flight Ops”
0x50	Command “Request PFP”

Discreet Movement Control
0x46	Command type “Flight Ops”
0x4D	Command “Discreet Movement”

0xDD	Direction:
0x46	Forward
0x52	Reverse
0x50	Port
0x53	Starboard

Request for Information (ROI)
0x46	Command type “Flight Ops”
0x49	Command “Request for information”
0xRR	Packet representing the desired information:
0x4C	Locartion
0x48	Heading/Speed/Altitude
0x5A	Attitude
0x42	Battery Status

Telemetry Data Packets (transmitted from Helicopter)

Location:
0x74	Report type “Telemetry”
0x4C	Report “Location”

0xDD	Degrees (0-180) Latitude
0xMM	Minutes (0-59) Latitude
0xSSSS	Seconds (0-59) Latitude. Use the upper six bits for integer portion of seconds, use remaining 10 bits for decimal portion of seconds. There are approximately 31 meters in one second of latitude (and slightly less in 1 minute of longitude at our distance from the equator). 31m / 2^10 = 3 cm accuracy, which is way more accuracy than the GPS will determine.
0xNS	0x4E = North
0x53 = South

0xDD	Degrees (0-180) Longitude
0xMM	Minutes (0-59) Longitude
0xSSSS	Seconds (0-59) Longitude. See above for more details.
0xEW	0x45 = East
0x57 = West

Heading/Speed/Altitude:
0x74	Report type “Telemetry”
0x48	Report “Heading, Speed, and Altitude”

0xHHHH	Hex value (0x0000 – 0x0167) representing current heading. Can potentially use extra bits for partial degrees.

0xSS	Hex value representing helicopter speed (m/s)

0xAAAA	2-byte value representing altitude in meters

Attitude
0x74	Report type “Telemetry”
0x5A	Report “Attitude”

0xRRRR	Hex value (0x0000 – 0x0167) representing current roll angle, can potentially use extra bits for partial degrees (increases as helicopter rolls in the starboard direction)

0xPPPP	Hex value (0x0000 – 0x0167) representing current pitch angle, can potentially use extra bits for partial degrees (increases as helicopter pitches forward)
0xYYYY	Hex value (0x0000 – 0x0167) representing current yaw angle, can potentially use extra bits for partial degrees (increases as helicopter rotates counter clockwise, as seen from above the helicopter)

Battery Status
0x74	Report type “Telemetry”
0x42	Report “Battery Status”

0xVVVV	Hex Value representing battery voltage

0xIIII	Hex Value representing helicopter current draw

0xTTTT	Hex Value representing battery temperature

On-board Error
0x74	Report type “Telemetry”
0x45	Report “Error”

0xEE	Hex value representing on of 128 error codes. (error codes to be determined)

Preflight Packet (PFP)
0x74	Report type “telemetry”
0x50	Report “Preflight Packet”

0xDD	Degrees (0-180) Latitude
0xMM	Minutes (0-59) Latitude
0xSSSS	Seconds (0-59) Latitude.
0xNS	0x4E = North
0x53 = South

0xDD	Degrees (0-180) Longitude
0xMM	Minutes (0-59) Longitude
0xSSSS	Seconds (0-59) Longitude. See above for more details.
0xEW	0x45 = East
0x57 = West

0xAAAA	Altitude reported by GPS

0xSSSS	Altitude reported by Sonar

0xVVVV	Battery Voltage

0xTTTT	Battery Temperature

0xSS	8-bit bit-field representing sensor status (1 = GOOD):
b7	b6	b5	b4	b3	b2	b1	b0
3-axis acc	2-axis gyro	1-axis gyro	Compass	GPS	Temp	uC